## Slide 1
FEASIBILITY
no new hardware · works with kits already purchased · a working core already exists
MEASURED — NOT PROJECTED
every figure below is produced by our own tools and reproducible from one command
TECHNICAL
– Phone camera + one printed card
– 0.50 ΔE2000 accuracy on 28 real camera sensors
– 379 automated tests, all passing
– Two independent verifiers that agree
ECONOMIC
– ≈ ₹5 per card, matte A4, 4-up
– No procurement, no new devices
– Reprints locally, no supply chain
– Kit-agnostic, no vendor lock-in
OPERATIONAL
– Runs fully offline (NDPS reality)
– Any issued Android handset
– Plugs into eSakshya / CCTNS-2.0
– Two frames ~10mm apart, ~8 seconds
CHALLENGES, AND WHAT WE DID ABOUT THEM
Replay: photographing a print or a screen
SOLVED. Two-view parallax against a folded 8mm tab. A print gives under 1% of the required depth.
A synchronised stereo replay
NOT SOLVED, and stated as such. Needs the genuine stereo pair and playback synced to a capture the attacker cannot time.
No public reagent dataset exists
Mitigated. Surrogate colour ladders. Substituting NCB standards is a data change, not an architecture change.
StrongBox missing on some issued handsets
Mitigated. TEE fallback, and the weaker guarantee is written into the record rather than glossed over.
Bad light producing a confident wrong answer
SOLVED. Quality gate + conformal abstention. All 83 stress conditions correctly handled — risky frames are refused, never guessed.
Colour accuracy on 28 real cameras
measured spectral sensitivities × CIE illuminants · quality-gate limit is 3.0 — every camera sits well inside it
The replay attack, refused
a print passes every colour check — it cannot fake depth
PHYSICAL CARD
28.1 px
99.6% of the 28.2 px the geometry predicts
LIVE
PHOTO-LAB PRINT
<1%
of the required depth
REFUSED
HIGH-DPI SCREEN
<1%
of the required depth
REFUSED
A flat reproduction cannot produce this at any print quality — flatness is the medium, not an artefact.
The simplest classifier wins — so there is no neural network
coverage on data the model never saw · no misclassifications on any held-out split
Nearest locus ΔE2000
Mahalanobis
Logistic regression
83 / 83
stress conditions correctly handled — every risky frame was refused, not guessed
94.5%
coverage under an illuminant the model never saw, and every miss was an abstention, never a wrong answer
28.1 vs 28.2 px
measured against predicted parallax on a physical card — the geometry matches to 99.6%
All figures are measured on synthetic frames or on measured spectral data. None is a field accuracy: no printed card has been photographed yet, and the capture matrix is the critical path.
Notes: Feasibility and viability summary: technical, economic, operational readiness on the left; measured evidence — colour accuracy, replay-attack refusal, classifier robustness, and headline achievements — on the right.