## Slide 1
The Record Is the Product — Not the Colour Reading
A presumptive field test, bound at capture into evidence a court can independently re-derive
HOW IT SOLVES THE PROBLEM
Admissibility
The problem statement says field results "cannot presently be relied upon as documentary evidence." We emit the BSA §63 certificate at the moment of capture.
§63 in force since 1 July 2024
Kit-agnostic
The reagent is declared by the operator, never read from a vendor's serialised pouch.
Works with kits already purchased
Honest uncertainty
Conformal prediction gives "inconclusive" a stated error bound, not a softmax percentage.
0 wrong calls under unseen light
Built for the field
Fully offline; records seal locally and queue for upload.
3.96 lakh NDPS cases pending
INNOVATION & UNIQUENESS
Two-view liveness
A photograph of a card passes every colour check. It cannot fake depth.
print 0.1 px vs 28.2 predicted
Two independent verifiers
Python and Dart, no shared code. A single implementation agreeing with itself proves nothing.
379 automated tests
A verifier that states its limits
Reports what is proven, what is asserted, and what is unverifiable.
3 buckets, not a green tick
No parallel evidence store
CCTNS-2.0 stays the system of record.
eSakshya handoff envelope
FROM SEIZURE TO COURT
1
Capture
card and strip in one frame, twice
2
Measure
fiducials → homography → CIELAB
3
Decide
prediction set with a stated α
4
Seal
SHA-256, signed in StrongBox
5
Verify
offline, by anyone, trusting no one
THE NUMBERS
EXTERNAL
3.96 lakh
NDPS cases pending
MHA, 2026
EXTERNAL
1,44,812
arrested under NDPS in 2022
NCRB, Crime in India 2022
EXTERNAL
65
exclusive NDPS courts, 22 states have none
MHA, 2026
EXTERNAL
₹2,080 cr
forensic modernisation spend
MHA, 2022
MEASURED BY US
0.50 ΔE
colour accuracy on 28 real cameras
our measurement
MEASURED BY US
₹5
per printed reference card
our costing
Notes: Idea title slide: how it solves the problem, innovation and uniqueness, the seizure-to-court process flow, and the key statistics.